## Slide 1
TOPOOPT
Co-optimizing Network Topology and Parallelization Strategy for Distributed Training Jobs
Shuyao Qi
Paper Sharing: NSDI 2023
16/03/2023

## Slide 2: Background
Previous proposals about Auto Parallel focus on co-optimizing computation and communication plan in distributed DNN training(FlexFlow, GSPMD, Automap, msr-fiddle, MindSpore)
Training workloads do not satisfy common assumptions about datacenter traffic that underlie the design of Fat-tree interconnects.

## Slide 3: Background -Distributed DNN training workload
The DNN training jobs are long-lasting and the traffic distribution can be pre-computed.
MP transfers: the network traffic created by the activations and gradients computed during the Forward and Backpropagation steps
AllReduce transfers: the network traffic created by synchronizing the model weights across accelerators in one iteration

## Slide 4: Background -Distributed DNN training workload

## Slide 5: System Design -TOPOOPT’s interconnect
Degree of each server: the number of interfaces on each server (denoted by d)
Direct-connect topology: optical switches connect the servers directly.
Host-based forwarding: The degree of each server is typically smaller than the total number of neighbors to communicate during training. Hosts can act as switches and forward incoming traffic towards the destination.
One-shot reconfiguration.

## Slide 6: System Design -Simple Introduction of Parallelization Strategy
SOAP: 4 parallelizable dimensions of DNN training

## Slide 7: System Design -Simple Introduction of Parallelization Strategy
Taskgraph

## Slide 8: System Design -Co-optimizing Parallelization Strategy and Network Topology
Alternating optimization
Finding the optimal parallelization strategy alone is an NP-complete problem. Let alone add network topology and routing to it
The search space is divided into 2 planes: Comp. ×Comm. and Comm. × Topo.
Comp. ×Comm. optimization is handled with Flexflow’s MCMC search algorithm

## Slide 9: System Design -Co-optimizing Parallelization Strategy and Network Topology
4 steps to optimize the comm.×topo. plan
Distribute the degree d between AllReduce and MP sub-topologies based on their share of total traffic
Construct the AllReduce sub-topology
Construct the MP sub-topology
Final topology and routing

## Slide 10: System Design -Construct the AllReduce sub-topology
Traffic Mutability and AllReduce Topology
AllReduce transfers are mutable whereas MP transfers are notConstruct the AllReduce sub-topology
simply permuting the label of the servers gives another ordering that will finish the AllReduce operation with the same latency while potentially providing a smaller hop-count for MP transfers.

## Slide 11: System Design -Construct the AllReduce sub-topology
Algorithm for building AllReduce sub-topology

## Slide 12: System Design -Construct the AllReduce sub-topology
TOPOOPT combines the three ring-AllReduce permutations to load-balance the AllReduce transfers while providing a short hop-count for MP transfers.

## Slide 13: System Design -Construct the MP sub-topology
Algorithm for building MP sub-topology

## Slide 14: Large Scale Simulation -Comparison with multiple topologies
Estimated cost of simulated topologies

## Slide 15: Large Scale Simulation -Comparison with multiple topologies
Performance of each topologies (single task)

## Slide 16: Large Scale Simulation -Comparison with multiple topologies
Performance of each topologies (multiple tasks)
number of tasks:
5,10,15,20,27
40% DLRM
30% BERT
20% CANDLE
10% VGG16
Faster than

## Slide 17: Impact of All-to-all traffic
TOPOOPT’s hostbased forwarding approach incurs bandwidth tax.
Happens in worst cases: large embedding tables are distributed on each server.

## Slide 18: Impact of Reconfiguration Latency
Reducing the reconfiguration latencyto 1 μs enables OCS-reconfig-noFW to match the performance of TOPOOPT. However, OCS-reconfig-FW still suffers from inaccurate demand estimations.